## Slide 1
Fast Fluid Dynamics
Wangda Zuo, Ph.D.
Associate Professor, Lewis-Worcester Faculty Fellow
Department of Civil, Environmental and Architectural Engineering
University of Colorado Boulder
Wangda.Zuo@Colorado.edu

## Slide 2: Indoor Environment Modeling Methods
Computational Fluid
Dynamics (CFD)
Multizone Model
 Little Information
Accuracy (Very Poor)
 Very Fast
Rich Information
Accuracy (Excellent)
 Very Slow
New Model
 Rich Information
Accuracy (Good)
Fast

## Slide 3: Fast Fluid Dynamics (FFD)
3
Semi-Lagrangian
Advection
Diffusion
& Source
Projection
Momentum

## Slide 4: FFD for Indoor Environment Modeling
2010
Jin and Zuo et al. (2012)
Improved FFD with local mass conservation method and a near-wall treatment for SL scheme
2007
2009
2001-2005
1999
Stam (1999)
First proposed the FFD method to produce plausible real-time fluid-like flows for computer graphics applications
Fedkiw et al. (2001)
Applied FFD to simulate smoke motions
Harris (2003)
Applied FFD to calculate cloud movements;
Liu et al (2004)
Applied FFD to compute the flow around complex obstacles
Harris (2005)
Implemented FFD on GPU
Zuo and Chen (2007)
First applied FFD for simulating indoor airflow for building simulation applications
Zuo and Chen (2009)
Systematically compared performance of FFD and CFD for indoor airflow simulation
Zuo and Chen (2010)
Applied FFD to simulate smoke transport in buildings
Zuo and Chen (2010)
Paralleled FFD on GPU to simulate indoor airflow
2011
Chronis et al. (2011)
Integrated FFD and GA for wind loading optimization
2012
2015
Healey and VanGilder et al. (2015)
First applied FFD to data center applications
2016
Zuo et al. (2016)
Implemented a FFD module in MBL for dynamically coupled simulation
Liu et al. (2016)
Implemented FFD in OpenFOAM for simulating indoor airflow
Xue et al. (2016)
Developed a new SL-based PISO for indoor environment modeling
2017
Tian et al. (2017)
Couple FFD and multizone airflow models
Liu et al (2017)
Developed a FFD-based adjoint method for inverse design of indoor environment
2018
Tian et al. (2018)
Intergraded FFD with an self-learning reduced order model ISAT
Liu and Chen (2018)
Developed a adaptive coarse grid generation method for FFD
2019
Tian et al. (2019)
Further investigated simulating data center airflow using FFD

## Slide 5: Example: Mixed Convection
5
Numerical Setting: 32 x 32 Grid, dt = 0.1s
Experimental Data: Blay et al (1992)
Flow in a Room with
Ventilation and Floor Heating
Mixed Convection
Blay, D., Mergui, S., and Niculae, C. 1992. "Confined turbulent mixed convection in the presence of horizontal buoyant wall jet", Fundamentals of Mixed Convection, 213, 65-72

## Slide 6: Mixed Convection: Results
Velocity
Temperature
6
Blay, D., Mergui, S., and Niculae, C. 1992. "Confined turbulent mixed convection in the presence of horizontal buoyant wall jet", Fundamentals of Mixed Convection, 213, 65-72

## Slide 7: Implementation of FFD on GPU
cudaMemcpy(vx, d_vx, sizeof(float) * geom.dimension, cudaMemcpyDeviceToHost);
…
cudaMemcpy(d_vy, vy, sizeof(float) * dimension, cudaMemcpyHostToDevice);
…
CUDA Codes
dim3 grid(imax/BLOCKDIM+ (!(imax%BLOCKDIM) ?0:1), jmax/BLOCKDIM+(!(jmax%BLOCKDIM)?0:1));
dim3 tids(BLOCKDIM, BLOCKDIM);
advect_k<<<grid, tids>>>(x, y, vx, vx0, vx0, vy0, imax, jmax, dt);
…
cudaMalloc((void**)&d_vx, sizeof(float) * dimension);
…
cudaFree(d_vx);
…
Program Flow
7

## Slide 8: Example: Lid-Driven Cavity Flow
Reference Data from Ghia et al.1982
8

## Slide 9: Simulation Speed
Lid-Driven Cavity Flow
Computing Time for 100 Time Steps
10 Seconds in Physical Process
CFD RNG k-e Model; FFD Laminar Model
CFD on CPU
FFD on CPU
50 x
30 x
1500 x
25 hours CFD on CPU = 1 minute FFD on GPU
FFD on GPU
9

## Slide 10: Example: Data Center Airflow Management
10
10
Side View of the Data Center
Plan View of the Data Center
    Location: Massachusetts
    Climate Zone: 5A – cool and humid
    Cooling System: chilled water system + ASE
On-site Photos

## Slide 11: Airflow Measurement
11
11
Snapshot of the results:
Measured Perforated Tile Airflow Rates
Measured Equipment Inlet Temperatures
Measured Rack Power Dissipation

## Slide 12: Model Validation: Plenum Airflow
12
Compare flowrates at tiles from FFD and CFD with measured data
Percentage Difference Range | FFD | CFD
 | No. of Tiles (Percentage) | No. of Tiles (Percentage)
 | 175 (95.6%) | 174 (95.1%)
 | 7 (3.9%) | 8(4.4%)
 | 1 (0.5%) | 1 (0.5%)
Total | 183 (100%) | 183 (100%)
Percentage Difference Range | FFD | CFD
 | No. of Tiles (Percentage) | No. of Tiles (Percentage)
 | 175 (95.6%) | 174 (95.1%)
 | 7 (3.9%) | 8(4.4%)
 | 1 (0.5%) | 1 (0.5%)
Total | 183 (100%) | 183 (100%)
Model DC Plenum Airflow

## Slide 13: Model Validation: Room Airflow
13
Compare rack-inlet temperatures from FFD and CFD with measured data
Percentage Difference Range | FFD | CFD
 | No. of Racks (Percentage) | No. of Racks (Percentage)
 | 95 (68%) | 107 (77%)
 | 37 (27%) | 28 (20%)
 | 17 (5%) | 14 (3%)
Total | 139 (100%) | 139 (100%)
Percentage Difference Range | FFD | CFD
 | No. of Racks (Percentage) | No. of Racks (Percentage)
 | 95 (68%) | 107 (77%)
 | 37 (27%) | 28 (20%)
 | 17 (5%) | 14 (3%)
Total | 139 (100%) | 139 (100%)
Model DC Room Airflow

## Slide 14: Bibliography
Zuo, W., Chen, Q. 2009. Real-time or faster-than-real-time simulation of airflow in buildings. Indoor Air 19(1): 33-44.
Zuo, W., Chen, Q. 2010. Simulations of air distribution in buildings by FFD on GPU. HVAC&R Research 16(6): 783-796.
W. Zuo, M. Wetter, W. Tian, D. Li, M. Jin, Q. Chen 2016. "Coupling Indoor Airflow, HVAC, Control and Building Envelope Heat Transfer in the Modelica Buildings Library.” Journal of Building Performance Simulation, 9(4), pp. 366-381.
W. Tian, J.W. VanGilder, X. Han, C.M. Healey, M.B. Condor, W. Zuo 2019. “A New Fast Fluid Dynamics Model for Data-Center Floor Plenums”. ASHRAE 2019 Winter Conference, January 12-16, Atlanta, GA.
W. Tian, T. A. Sevilla, D. Li, W. Zuo, M. Wetter 2018. "Fast and Self-Learning Indoor Airflow Simulation Based on In Situ Adaptive Tabulation." Journal of Building Performance Simulation, 11(1), pp. 99-112.
Performance Simulation, 11(1), pp. 99-112.